## Slide 1: Fasteners
Used to join together the various parts of the automobile.
Spot Welding
Soldering
Nuts & Bolts
Washers
Screws
Clips
Clamps
Studs
Rivets
Studs
Splines/Keys/RollPins
Glue/Silicone/Adhesives
Crimped (Body seams, electrical connections)

## Slide 2: Fasteners
External Threads (Male Threads)
Bolts, Studs, Screws
Internal Threads (Female Threads)
Nuts, Threaded holes

## Slide 3: Fasteners
Imperial Threaded Fasteners
UNC – Unified National Coarse.
UNF – Unified National Fine.

## Slide 4: Fasteners
Fine Threaded Fasteners
Stronger Thread
Less likely to come loose
Slow to assemble
Easier to ruin the thread (cross thread)
Imperial threaded fasteners come in inch increments.
½”, 5/16”, 3/8”, 7/16” …

## Slide 5: Fasteners
5/16” UNC X 1 ½” Bolt
Diameter
Coarse
1 ½” Long

## Slide 6: Fasteners
5/16” - 13 X 1 ½” Bolt
Major Diameter
13 Threads/inch
Total Length

## Slide 7: Fasteners
Bolt Grading (Strength)
Add 2 to the number of lines
Grade 8
Grade 5
Grade 2

## Slide 8: Fasteners
Metric Threaded Fasteners
ISO Metric – International Organization for Standardization
Most new vehicles have metric fasteners
M6, M7, M8, M10, M12, M14 …
M8 X 25 X 1
Metric
8mm
25mm long
Pitch (threads are 1mm apart)

## Slide 9: Fasteners
Imperial
Metric
Black/Silver in colour
Gold, red, green, yellow, etc.
Lines on the head
Numbers on the head
UNC, UNF
ISO metric
Standard tools (inch)
Metric tools (mm)
In inches
In millimeters

## Slide 10: Nuts
Hex Nut – Most common on automobiles.
Castle Nut – locks with a cotter pin
Wing Nut – No tool required
Locking Nut – Nylon Patch (center, top)
Lug Nut – Taper face to help center the wheel
Speed Nut – Push-on (mostly screws)

## Slide 11: Screws
Machine Screws –
no nut required ( usually less then ¼”
Passes through one piece and threads into other.
Sheet Metal Screws(self tapping) –
makes its own hole/threads
Set Screw – (allen wrench/no head)
Used for aligning pullies on the shaft.

## Slide 12: Washers
Flat Washer –
Distributes pressure over a wider surface area.
Lock Washer - Prevents the fastener from loosening.
Used at high vibration places.
Bites into the material and the fastener.

## Slide 13: Fasteners
Roll-pins/Spring-pins aligns + locking devices driven into a hole to
Lock a pulley or a spline.

## Slide 14: Fasteners
C - Clips
Internal C-Clip
External C-Clip
Snap Ring Pliers

## Slide 15: Fasteners
Basic Rules
Use correct length and thread.
Start threads by hand (no tool).
Install all bolts before final tightening any one on a single part.
Tighten all installed fasteners before leaving or leave a note
NOT TIGHT
Tighten evenly to a correct torque specification
and in proper sequence.

## Slide 16: Fasteners
Tightening Wheels
Tightening multiple bolts