## Slide 1: Unit 4 - Digital Multimeter Voltage Testing
When you complete this unit, you will be able to:
  Identify the voltage testing settings on the rotary dial
  Explain the advantage of using the millivolt setting when possible
  Demonstrate how to switch between AC and DC voltage testing

## Slide 2
The meter MUST be connected in Parallel when preforming voltage tests
This requires a completed circuit which the meter can then be connected to as an additional branch circuit
This is why high impedance is important, so the circuit is minimally impacted
Digital Multimeter Voltage Testing

## Slide 3
3
AC Voltage Testing
  Connect the red test lead to the VΩHz terminal
  Connect the black test lead to test lead to the COM terminal
  Move the Rotary Dial to AC Volts
Digital Multimeter Voltage Testing
Notes: The next slide illustrates the proper signal generator connections and test

## Slide 4
4
AC Voltage Testing
Connect the red test lead to test terminal #5 (AC sine wave)
Connect the black test lead to test terminal #6 (ground)
Turn the simulator ON (press on/off button)
Rotate the middle dial B
Watch the changing voltage values on both the digital display and analog bar
Digital Multimeter Voltage Testing
#5
#6
This completes the AC Volt Test
B

## Slide 5
5
DC Voltage Testing
  Connect the red test lead to the VΩHz terminal
  Connect the black test lead to test lead to the COM terminal
  Move the Rotary Dial to DC Volts
Digital Multimeter Voltage Testing
Notes: The next slide illustrates the proper signal generator connections and test

## Slide 6
6
DC Voltage Testing
Connect the red test lead to test terminal #4 (DC voltage)
Connect the black test lead to test terminal #6 (ground)
Turn the simulator ON (press on/off button)
Rotate dial C
Watch the changing voltage values on both the digital display and analog bar
Digital Multimeter Voltage Testing
#4
#6
This completes the DC Volt Test
C

## Slide 7
7
AC/DC millivolt Testing
  Connect the red test lead to the VΩHz terminal
  Connect the black test lead to test lead to the COM terminal
  Move the Rotary Dial to AC/DC millivolts
  Rotate dial C all the way to the left
Digital Multimeter Voltage Testing
C
Notes: The next slide illustrates the proper signal generator connections and test

## Slide 8
8
DC millivolt Testing
Connect the red test lead to test terminal #4 (DC voltage)
Connect the black test lead to test terminal #6 (ground)
Turn the simulator ON (press on/off button)
Slowly rotate dial C
Watch the changing voltage values on both the digital display and analog bar
Digital Multimeter Voltage Testing
#4
#6
This completes the DC millivolt Test
C

## Slide 9
AC millivolt Testing
  Rotate dial B all the way to the left
  Connect the red test lead to test terminal #5 (AC voltage)
  Press the AC/DC button
  Slowly rotate dial B
  Watch the changing voltage values on both the digital display and analog bar
Digital Multimeter Voltage Testing
#5
#6
This completes the AC millivolt Test
B

## Slide 10: Review for Understanding
When testing for DC Voltage which rotary dial setting is used?
When testing for AC Voltage which rotary dial setting is used?
Why would you use the millivolt (mV) setting?
How do you switch between testing AC millivolts and DC millivolts?
Notes: Answers:
The second setting: Volts DC (V with a straight line and 3 dashed underneath)
The first setting: Volts CC (V~ with a wavy line ~)
If measuring a small voltage (millivolts) this setting will be more accurate than the standard voltage setting.
Press the AC/DC button